| MEDIA RELEASE | January 2015 |
| --- | --- |

# Janisol 2 EI30 fire protection sliding doors:

Extremely slender fire protection profile

Barrier-free systems for high-footfall buildings such as shopping centres, underground car parks, stations and other public or 
private buildings are increasingly fitted with automatically opening sliding doors. Janisol 2 EI30 fire protection sliding doors by Jansen unite operational reliability with a high standard of design.

With its refined sensor technology, the sophisticated system concept offers high security and – because the fire protection sliding doors are activated automatically – a new level of convenience. Ease of manufacture is a further impressive advantage. Thanks to the new special profile filled with ceramic compound for the outer and vent frames, no complex work is necessary for the sheet edge, and no additional fire-resistant panels are required. There is also no need for a floor guide in the entrance 
area.

With face widths of only 25 and 50 mm for the door leaf and door frame profiles respectively, the Janisol 2 EI30 is without doubt the slenderest fire protection profile currently on the market. The steel profile system for single- or double-leaf fire protection sliding doors with or without an emergency exit function has been tested with a large selection of drive motors (Tormax, GEZE, Gilgen Door Systems AG, Dorma and Record), glazing units (Fireswiss Foam from Glas Trösch, Pyrostop from Pilkington, Pyrobel from AGC, Contraflam from Verotech, Pyranova from Schott and single pane fire-resistant glass from Arnold-Fire or Hero-Fire) and panels. The maximum leaf sizes are 1400 x 2500 mm and 2800 x 2500 mm.

About Jansen AG
Jansen AG was founded in Oberriet in Switzerland in 1923 and develops, manufactures and supplies welded and drawn precision steel tubes and steel profile systems as well as plastic products for the construction sector and industrial applications. Since 1978, Jansen has also been the exclusive Swiss distribution partner of Schüco International KG and sells the German company's aluminium and timber/metal profile systems for the construction industry. The Jansen Group is still fully family owned. The very latest production facilities and continuous investment in quality assurance and employees have earned Jansen products a name synonymous with Swiss quality and innovation all over the world. The Jansen Group has a global workforce of around 900. The company achieved a turnover of CHF 280 million in 2014.

Contact for editorial matters:

Jansen AG

Stefani Zemp

Industriestrasse 34

CH-9463 Oberriet SG, Switzerland

Tel.: +41 (0)71 763 96 72

Fax: +41 (0)71 763 91 13

e-mail: stefani.zemp@jansen.com

Photo credits: Jansen AG

Publishing these photographs must be in connection with the above media release.

Barrier-free passageways are increasingly fitted with automatically opening sliding doors.

Janisol 2 EI30 fire protection sliding doors unite operational reliability with a high standard of design.

3D schematic fire protection sliding door without breakout

3D schematic fire protection sliding door with breakout