| MEDIA RELEASE | January 2015 |
| --- | --- |

Janisol Arte now also suitable for sliding doors:

# Attractive profile system for new buildings and refurbishments

Architects are increasingly discovering the advantages of Janisol Arte – a thermally broken steel profile system, which Jansen developed originally for the reconstruction of historical windows – in the configuration of large facade openings in new buildings. The most recent system addition for sliding doors and pivoting windows presented at BAU 2015 expands the scope of application of this extremely slender steel profile system.

The extremely slender Janisol Arte steel profile system is perfect for creating glazing installations with graceful grid dimensions and outstanding strength. In addition to windows and fixed glazing, the system can also be used for sliding leaves up to 3000 mm wide x 2500 mm high (max. 150 kg/leaf). Double-glazed insulating glazing 20 to 34 mm thick can achieve a UW value of 1.5 W/m2K. The Janisol Arte sliding door has been tested and carries a CE marking. The materials used – steel and glassfibre-reinforced high-performance plastics – are tremendously robust, which results in a very strong and durable construction. The range of application will be extended during 2015 to include pivoting windows.

The Janisol Arte steel profile system for windows and glazing achieved CE classification in accordance with EN 14351-1 with excellent test results. With a profile face width of between 25 and 40 mm and an installed depth of 60 mm, it can be used to reproduce historical window constructions true to the original or to develop contemporary solutions. Window sizes up to 800 by 1600 mm are possible – as single or double side-hung windows, as single- or double-sash side-hung windows opening inwards or outwards, as single-sash bottom- or top-hung windows or as single-sash projected top-hung windows, again opening inwards or outwards, while fully meeting today's requirements for the thermal insulation of buildings. The system can also fulfil other modern standards, such as those for sound insulation.

The multiple award-winning Janisol Arte profile system is based on a completely new type of profile and connection technology that was developed in-house at Jansen and has been tested in accordance with EN 14024. The modular system offers architects and planners a wide range of solutions for all types of facade, window and door constructions – always taking all structural engineering, building physics, safety and security requirements set by the regulations and the client into account.

About Jansen AG
Jansen AG was founded in Oberriet in Switzerland in 1923 and develops, manufactures and supplies welded and drawn precision steel tubes and steel profile systems as well as plastic products for the construction sector and industrial applications. Since 1978, Jansen has also been the exclusive Swiss distribution partner of Schüco International KG and sells the German company's aluminium and timber/metal profile systems for the construction industry. The Jansen Group is still fully family owned. The very latest production facilities and continuous investment in quality assurance and employees have earned Jansen products a name synonymous with Swiss quality and innovation all over the world. The Jansen Group has a global workforce of around 900. The company achieved a turnover of CHF 280 million in 2014.

Contact for editorial matters:

Jansen AG

Stefani Zemp

Industriestrasse 34

CH-9463 Oberriet SG , Switzerland

Tel.: +41 (0)71 763 96 72

Fax: +41 (0)71 763 91 13

e-mail: stefani.zemp@jansen.com

Photo credits: Jansen AG

Publishing these photographs must be in connection with the above media release.

Janisol_Arte_3D.tif:

With a visible profile width of between 25 and 40 mm and an installation depth of 60 mm, Janisol Arte is the first steel profile system for loft and industrial glazing to be this slender and still incorporate a thermal break. (System section: Jansen)

Janisol Arte sliding door

Commercial building (listed warehouse)

Zürcher Strasse, St.Gallen

Client: St.Gallen Building Department

Architect (refurbishment): Wehrli Architekten AG, St.Gallen, Switzerland

Pumping station Schönau

Client: Wasserverbund Region Bern (WVRB) AG, Bern, Switzerland

Architect: Markus Tschantré, Bern, Switzerland