| MEDIA RELEASE | January 2015 |
| --- | --- |

Janisol HI for windows and doors:

# High steel strength with high insulation 
performance

Jansen rises to the challenge of increasing requirements for the thermal insulation of buildings with Janisol HI, a highly insulated steel profile system for windows and doors. The system's extremely narrow profile face widths make it suitable for manufacturing a wide range of window and door elements and fixed 
glazing units. In addition, Jansen launched the Janisol HI folding partition at BAU 2015. This product combines the excellent thermal insulating properties of the proven steel profile system with high sound insulation (up to 45 dB).

The excellent thermal insulating performance of the Janisol HI steel profile system owes much to its insulating bars made from glassfibre-reinforced polyurethane. Janisol HI steel doors achieve UD values up to 1.0 W/m2K and have earned the MINERGIE® label. With an installation depth of only 80 mm, these doors can accommodate infill units up to 56 mm thick. The high thermal insulation values go hand-in-hand with high mechanical strength. Therefore Janisol HI steel doors are perfect in particular for high-footfall entrance areas, where they can be relied on to function perfectly and reliably in the long term. A new addition to the range is a profile for sheet metal-clad doors, which further expand the possible uses of this highly thermally insulated steel profile system.

Large facade openings

for a contemporary architectural language

Steel windows and fixed glazing in Janisol HI also score well when it comes to excellent thermal and structural properties. Janisol HI fixed glazing units achieve Uw values as low as 0.69 W/m2K, while the system's windows – including side-hung, turn-tilt, double-leafed and top-hung – go as low as 0.8 W/m2K. To show that the HI system can live up to this promise, it carries the Minergie certification of Janisol HI windows in Switzerland – the first steel window to do so.

Sash heights of up to 2800 mm and weights up to 180 kg are possible with Janisol HI for an installed depth of 90 mm. Infill elements thicknesses of up to 66 mm (e.g. triple glazing, burglar-resistant glass) can be used. At the same time, the narrow profiles allow the maximum amount of daylight to enter, which reduces the use of artificial lighting. The distinctive design freedom offered by Janisol HI makes it the preferred system solution for up-market residential buildings.

Simple construction thanks to proven system technology

Processors benefit from practical system components that promise simple and efficient processing. For example, installing a lock into a door takes only a few minutes because the lock is integrated into the isolator, which does away with the need for laborious steel machining. No additional profiles are required for the highly insulated system solution because the centre gasket attaches directly to the profile frame.

With Janisol HI, Jansen offers an innovative solution capable of impressing architects, window and facade builders and clients alike: along with great design freedom, cost-efficient manufacture and excellent thermal insulation performance, Janisol HI steel profiles show off their style to best effect in any situation.

About Jansen AG
Jansen AG was founded in Oberriet in Switzerland in 1923 and develops, manufactures and supplies welded and drawn precision steel tubes and steel profile systems as well as plastic products for the construction sector and industrial applications. Since 1978, Jansen has also been the exclusive Swiss distribution partner of Schüco International KG and sells the German company's aluminium and timber/metal profile systems for the construction industry. The Jansen Group is still fully family owned. The very latest production facilities and continuous investment in quality assurance and employees have earned Jansen products a name synonymous with Swiss quality and innovation all over the world. The Jansen Group has a global workforce of around 900. The company achieved a turnover of CHF 280 million in 2014.

Contact for editorial matters:

Jansen AG

Stefani Zemp

Industriestrasse 34

CH-9463 Oberriet SG, Switzerland

Tel.: +41 (0)71 763 96 72

Fax: +41 (0)71 763 91 13

e-mail: stefani.zemp@jansen.com

Photo credits: Jansen AG

Publishing these photographs must be in connection with the above media release.

Janisol HI folding partition

Janisol HI window construction

Janisol HI door construction

With the Janisol HI steel profile system for windows and doors, 
Jansen is setting new standards in thermal insulation.