| MEDIA INFORMATION | January 2017 |
| --- | --- |

Jansen VISS roof glazing:

Wide range of versions in spite of reduced complexity

# One solution – two requirements –

# many possibilities

The Jansen VISS steel roof glazing system can be used to design many different versions of standard or fire protection glazed roof solutions, in the form of flat roofs, pyramid roofs, shed roofs or hipped roofs. The construction of the tested heavy-duty steel construction is based on just a few system components – a cost-efficient advantage for the design and assembly. Example: only four additional components are needed to turn a standard glass roof into a fire-rated glass roof. The highly insulated steel profile system is also highly efficient in terms of thermal insulation; it achieves excellent Uf-values of up to 0.53 W/(m2K). As a fire-rated solution, it also covers fire protection to loadbearing members: REI30, REW30, REI60, REW60.

Secure investment

• The tested system solution guarantees low-maintenance glazed roof constructions with a long service life

• Tested standard and fire-rated applications with close reference to EN 13830

• Excellent performance characteristics: air permeability 750 Pa, tightness against heavy rain 1200 Pa at 3 litres m3/min, wind load resistance up to 2000 Pa

Design advantages

• System suitable for flat roofs, pyramid roofs, shed roofs and hipped roofs, hence offering wide range of design options

• All constructions can be designed as standard roof glazing or as fire-rated roof glazing

• Maximum glass format for fire-rated glazing: 1250 mm x 3050 mm

• Fire-rated application: roof slope from 0 to 80 degrees at Uf-values up to 0.53 W/(m2K)

• Different types of fire-rated glass can be used: project-specific requirements can be covered using glass from four different glass manufacturers

Assembly advantages

• Optimised system with respect to assembly and cost-efficiency

• Low number of components facilitates innovative detail solutions

• Easy assembly: no continuous bolt rebate profile, optimised cross-point design, identical external bolt seals (top and bottom seals)

• Reduced number of components ensures optimised stock holding

• A number of different fire-rated glass types can be used to suit specific country regulations and to reduce costs.

Photo credits: Jansen AG

Including the images in editorial publications is tied to this media information.

Rend-VISS-Dach.jpg

About Jansen AG
Jansen AG, founded in 1923 and based in Oberriet, Switzerland, develops, manufactures and markets welded and drawn precision steel tubing, steel profile systems and plastic products for the construction industry and wider industrial use. Since 1978, Jansen has also been the exclusive Swiss sales partner of the German firm, Schüco International KG, marketing its aluminium profile systems for the construction sector. Even today, the Jansen Group remains a 100% family-owned concern. The very latest production facilities and continuous investment in quality assurance and employees have earned Jansen products a name synonymous with Swiss quality and innovation all over the world. The Jansen Group has a global workforce of around 950.

Contact for editorial matters:

Jansen AG

Stefani Zemp

Industriestrasse 34

CH-9463 Oberriet SG, Switzerland

Tel.: +41 (0)71 763 96 72

E-mail: stefani.zemp@jansen.com

BAUtext Mediendienst München

Anne-Marie Ring

Wilhelm-Dieß-Weg 13

DE-81927 Munich

Tel.: +49 (0)89 21 11 12 06

E-mail: a.ring@bautext.de